## Slide 1
Ground Penetrating Radar (day 3)
EOSC 350 ‘06
Slide 1

## Slide 2
From Last Time
Common Offset
Common Midpoint
Transillumination

## Slide 3
From Last Time
Shorter pulses contain a wider range of frequencies
Shorter pulse overall contain higher frequencies
Spatial length increases as pulse length increases

## Slide 4
From Last Time
There is a compromise between resolution and probing distance: Higher frequencies Better resolution Layers: Objects: Higher frequencies Lower probing distance

## Slide 5
From Last Time

## Slide 6
Today’s Topics
Interpretation and some examples

## Slide 7
Example: Potash Mine
Water was leaking into the potash mine Reducing structural integrity of mine shafts Want to know where water is and its source Water infiltration produces a strong reflector

## Slide 8
Example: Potash Mine
Zero offset survey performed.
Arrival time to depth conversion performed Q: Without a direct ground wave measurement or hyperbola to obtain propagation speed, how could they do conversion?

## Slide 9
Example: Potash Mine
A: Potash in an anhydrite mineral. From known physical properties, V ~ 0.13 m/ns da = Vt/2

## Slide 10
Example: Potash Mine
Q: What kinds of features do you see in the data?

## Slide 11
Example: Potash Mine
Strong reflector from intruding water (7 - 8 m from shaft)
Water is delineated and seems to be coming from the right
Ringing from mine infrastructure

## Slide 12
Example: Underground Storage Tanks
Diagram of problem
Want to locate a set of underground storage tanks. Q: What direction would you orient your survey lines? Why? Q: What features do you expect in your radargram?
Notes: A: Perpendicular to the tanks lengthwise. Because it will act hopefully as a point reflector.
A: Something like a hyperbola.

## Slide 13
Example: Underground Storage Tanks
Q: If tanks too big to be point reflectors, can you still obtain layer velocity? How?
Q: How can you figure out the horizontal location and depth to each tank? (assume you know the velocity)
Q: Why aren’t signatures from tank beds entirely visible?
Notes: A: Yes. Use their slope.
A: Top of hyperbola is over top of the tank. Eq for shortest travel time can be used to get depth.
A: Tanks are conductive metal so no signal gets through and reflects of beds at certain orientations.

## Slide 14
Example: GPR App Problem
Zero offset survey
Two buried reflectors
Wave regime!!!

## Slide 15
Example: GPR App Problem
Q1: From the radargram, use the slope to determine the propagation velocity.
Q2: From the preset parameters, compute the probing distance (or DOI) using the quasi-static AND wave regime approximation. Compare to the DOI in the app. What regime are we in?
Q3: Determine the relative permittivity of the host media from the medium velocity you computed. Does it match the value set in the app?

## Slide 16
Example: GPR App Problem
Q1: From the radargram, use the slope to determine the propagation velocity.
Q2: From the preset parameters, compute the probing distance (or DOI) using the quasi-static AND wave regime approximation. Compare to the DOI in the app. What regime are we in?
Q3: Determine the relative permittivity of the host media from the medium velocity you computed. Does it match the value set in the app?

## Slide 17
Example: GPR App Problem
Q1: From the radargram, use the slope to determine the propagation velocity.
Q2: From the preset parameters, compute the probing distance (or DOI) using the quasi-static AND wave regime approximation. Compare to the DOI in the app. What regime are we in?
Q3: Determine the relative permittivity of the host media from the medium velocity you computed. Does it match the value set in the app?

## Slide 18
Example: GPR App Problem
Q1: From the radargram, use the slope to determine the propagation velocity.
Q2: From the preset parameters, compute the probing distance (or DOI) using the quasi-static AND wave regime approximation. Compare to the DOI in the app. What regime are we in?
Q3: Determine the relative permittivity of the host media from the medium velocity you computed. Does it match the value set in the app?

## Slide 19
Example: GPR App Problem
Q1: From the radargram, use the slope to determine the propagation velocity.
Q2: From the preset parameters, compute the probing distance (or DOI) using the quasi-static AND wave regime approximation. Compare to the DOI in the app. What regime are we in?
Q3: Determine the relative permittivity of the host media from the medium velocity you computed. Does it match the value set in the app?

## Slide 20
Example: GPR App Problem
Q4: What is the horizontal resolution of the survey at a depth of 4m? Adjust the location of the reflectors to confirm this with the app.
Q5: How could we improve the survey resolution? What drawback might this have?
Q6: If we increases the radius of one of the reflectors, what happens to its signature?

## Slide 21
Example: GPR App Problem
Q4: What is the horizontal resolution of the survey at a depth of 4m? Adjust the location of the reflectors to confirm this with the app.
Q5: How could we improve the survey resolution? What drawback might this have?
Q6: If we increases the radius of one of the reflectors, what happens to its signature?

## Slide 22
Example: GPR App Problem
Q4: What is the horizontal resolution of the survey at a depth of 4m? Adjust the location of the reflectors to confirm this with the app.
Q5: How could we improve the survey resolution? What drawback might this have?
Q6: If we increases the radius of one of the reflectors, what happens to its signature?

## Slide 23
Example: GPR App Problem
Q4: What is the horizontal resolution of the survey at a depth of 4m? Adjust the location of the reflectors to confirm this with the app.
Q5: How could we improve the survey resolution? What drawback might this have?
Increase frequency  Reduces probing distance
Q6: If we increases the radius of one of the reflectors, what happens to its signature?

## Slide 24
Example: GPR App Problem
Q4: What is the horizontal resolution of the survey at a depth of 4m? Adjust the location of the reflectors to confirm this with the app.
Q5: How could we improve the survey resolution? What drawback might this have?
Increase frequency  Reduces probing distance
Q6: If we increases the radius of one of the reflectors, what happens to its signature?
No longer a hyperbola, slope trick works, early observed signals.

## Slide 25
Concluding Thoughts: GPR in a Nutshell
Electromagnetic Method
Exploits contrasts in dielectric permittivity and conductivity
Sends a pulse of radiowaves into the ground
Signals reflect, refract and transmit at interfaces
Measured signals represented using radargrams

## Slide 26
Concluding Thoughts: When to use GPR
Generally near-surface applications (10s metres or less)
Images the interfaces which define subsurface structures
Examples: - Geotechnical problems (rock fractures, slope stability …) - Find buried infrastructure (pipes, wires, storage tanks …) - Near surface soil properties and structures - Forensics - Archaeology

## Slide 27
Concluding Thoughts: Planning a Survey
What do I know about the local physical properties?
How deep do I need to image?
What are the dimensions and separations of structures I want to image? Allows you to pick optimum grid spacing and operating frequency

## Slide 28
Concluding Thoughts: Optimum Frequency
Resolution: Layers Objects
Probing Distance:
Choice in operating frequency is a compromise between resolution and probing distance!!!!

## Slide 29
Concluding Thoughts: What to Look For
Hyperbolas
Linear
Features
Geometry can give us layer velocities, location of objects and depths of interfaces.

## Slide 30
Questions About GPR?